## Slide 1
Medicine Box AI Recognition System
Mid-Progress Presentation | Grove Vision AI V2 + Host Camera Hybrid Pipeline | May 2026
Edge-side medicine box detection with Grove Vision AI V2, combined with host-side HD barcode & OCR recognition.
264+56
Synthetic medicine_box images
2+1
Detector classes: barcode, text, medicine_box
10/10
Real E2E validation images
2
Cameras: Grove + HD Host

## Slide 2
Background and Problem
2
Why medicine-box recognition needs a hybrid edge-host approach
The Challenge
Medicine packages contain critical safety information: drug name, barcode, specification, approval number, batch number, and expiry date.
Manual reading is slow and error-prone, especially for elderly users or those with visual impairment.
Existing solutions require high-end smartphones or dedicated scanners — not suitable for low-cost edge deployment.
Key Insight
Grove Vision AI V2 (240x240 camera) cannot resolve small barcode lines or Chinese text for OCR.
However, it CAN reliably detect whether a medicine box is present — making it an ideal edge-side trigger.
A host camera (1080p+) handles the actual barcode decoding and OCR — forming a practical hybrid system.

## Slide 3
Aim and Objectives
3
Research aim and mid-progress scope
Research Aim
Design and evaluate a practical system for recognizing medicine-box barcode and text using a hybrid edge-host architecture, combining Grove Vision AI V2 as an edge trigger with a host-side HD camera for high-accuracy OCR.
Mid-Progress Objectives
Obj 1 — Edge Detection: Train and deploy a single-class medicine_box detector on Grove Vision AI V2 for real-time box presence detection.
Obj 2 — Host Recognition: Build a host-side pipeline for HD barcode detection + OCR text recognition + structured medicine info extraction.
Obj 3 — Hybrid Integration: Connect edge and host into a unified demo where Grove triggers the host camera pipeline.

## Slide 4
System Architecture
4
Hybrid edge-host pipeline: Grove triggers, Host recognizes
Grove Vision AI V2 — Edge Trigger
Camera: 240x240 onboard sensor
Model: medicine_box single-class detection
Output: [x, y, w, h, score, target=0]
Role: Detect if medicine box is present
Does NOT: read text, decode barcode, run OCR
Host Computer — Main Recognition
Camera: Mac/USB 1080p+ HD camera
Detector: barcode + text dual-class CNN
OCR: Tesseract + custom medicine classifier
Output: Structured JSON + preview image
Role: Full barcode decoding and text recognition

## Slide 5
Dataset and Annotation
5
Synthetic + real data across two detection tasks
Grove medicine_box
264 train / 56 val images
Synthetic, 1 class
Trained on SenseCraft AI
Host barcode/text
2000 train / 400 val
Synthetic v3, 2 classes
10 drug types, auto-labeled
Real validation
76 train / 14 val
barcode + text labels
Manual annotation
Host OCR Dataset
Synthetic: 15,962 train OCR crops + 3,198 val crops (10 drug types, Chinese + English labels)
Real: 228 train crops + 42 val crops (manual CSV annotations)
Generator: capsule icons, barcodes, foil strips, 7 background themes, glare, occluders
Annotation Quality
medicine_box: auto-generated bounding boxes from known box position
barcode/text: YOLO-format labels auto-generated per scene element
Real images: manually annotated with labelImg

## Slide 6
Grove Vision AI V2 — Edge Implementation
6
Single-class medicine_box detection on low-power MCU
Model Deployment Pipeline
1. Generate synthetic medicine_box images with auto-annotation (264 train / 56 val)
2. Train Swift-YOLO single-class model on SenseCraft AI (imgsz=192, int8 + Vela)
3. Flash to Grove via Python deploy script (XMODEM over USB serial)
4. Verify: AT+INVOKE returns boxes with label=medicine_box
AT Command Interface
AT+INVOKE: triggers single inference, returns JSON with boxes array
AT+INFO: writes model metadata (class names, model name)
Output format: [x_center, y_center, width, height, score, class_id]
Box coordinates normalized to [0, 240] pixel space
Flashing Script — Key Technical Achievements
Fixed 6 critical bugs in the Python XMODEM flashing pipeline: pyserial RTS/DTR initialization, block-number wrapping after 255, post-config bootloader re-entry with 1-char triggers, menu-based post-transfer flow ([0] Reboot / [1] Xmodem), non-standard EOT handling, and AT+INFO metadata write after reboot. The script now reliably flashes 920KB~2.8MB models in 2~20 minutes.

## Slide 7
Host-Side Pipeline — Barcode & OCR
7
High-resolution camera + barcode/text detector + OCR + classifier
Detection Module
Custom lightweight CNN (Conv2D + SeparableConv2D backbone)
4 downsampling stages, stride-16 YOLO-style grid output
2 classes: barcode + text, trained on synthetic v3 + fine-tuned on real
Image size: 320x320, batch size: 16, epochs: 120
OCR & Classification
OCR crops extracted from text detection regions
Tesseract OCR for Chinese + English recognition
Custom medicine classifier: matches recognized text to drug database
10 drug entries with Chinese/English names, manufacturer, spec
Pipeline Results
Synthetic detector: barcode F1=0.843, text F1=0.613 at threshold 0.25. Real-image test on frame_00000: 11 detections (1 barcode at score 0.646 + 10 text regions). OCR tested on 96 real medicine box images with structured JSON output including drug name, barcode digits, specification, and approval code.
End-to-end: pipeline outputs JSON + annotated preview image per frame. Pipeline verified working on host_session_001 captures.

## Slide 8
Key Issues and Design Decisions
8
What changed after experiments and testing
Issue 1: Grove camera resolution limit
Grove Vision AI V2 camera is 240x240 — too small for barcode fine lines and Chinese small-font OCR. Cannot replace host camera for recognition tasks.
Decision: Hybrid architecture
Split the system: Grove detects medicine_box presence (edge trigger), host camera handles all barcode/OCR (main recognition). This preserves edge-AI value while making recognition practical.
Issue 2: YOLOv8 → Grove incompatibility
YOLOv8 int8 quantization fails with TF converter (CONCAT ops). Vela reports 0% NPU usage for float32 models. Output format [1,5,756] incompatible with Grove's SSCMA firmware.
Decision: SenseCraft Swift-YOLO
Train directly on SenseCraft AI platform using Swift-YOLO architecture. Outputs Grove-compatible int8+vela TFLite with decoded [x,y,w,h,score,target] boxes.
Issue 3: OCR domain gap
TF OCR trained on synthetic data performs poorly on real captured crops. Tesseract is currently more robust for real-image Chinese text recognition.
Decision: Tesseract fallback
Use Tesseract as primary OCR engine for real images while continuing to improve TF OCR on augmented real data.

## Slide 9
Next Steps and Timeline
9
Work plan for completion
Now
Collect more real medicine-box images from multiple products. Improve medicine_box model with real data fine-tuning. Verify Grove detection with diverse box types and lighting conditions.
Week 1-2
Enhance host-side pipeline: improve barcode/text detector F1 on real images. Add structured field extraction (drug name, barcode, batch, expiry). Add multi-language OCR support.
Week 3
Build unified hybrid demo with automatic Grove→Host trigger. Test end-to-end accuracy on 20+ real medicine boxes. Profile latency: Grove detection + host capture + full pipeline.
Week 4
Prepare dissertation: experiments, figures, ablation studies, limitations. Record final demonstration video. Write conclusion and future work.

## Slide 10
Q & A
Thank you for your attention.
Demo: Grove edge detection (medicine_box) → Host camera barcode + OCR → Structured JSON output Research focus: hybrid edge-host architecture for practical medicine-box AI recognition